## Slide 1: Parameterized Quantum Pulse Circuit and its Application

## Slide 2: 1.1 Towards Parameterized Quantum Pulses Advantage Speaker: Zhiding Liang (University of Notre Dame)
1.2 Code Demo: Build Your Own Parameterized Pulses on Qiskit Dynamics and TorchQuantum
Mentor: Jinglei Cheng (Purdue University)
Session 1
1.3 Hybrid Gate – Pulse Model for Variational Quantum Algorithms Speaker: Jinglei Cheng (Purdue University)
2.1 qutip-qip: Pulse-level Circuit Simulation Speaker: Boxi Li (Forschungszentrum Jülich)
2.2 Code Demo: Pulse level Circuit Simulation on qutip
Mentor: Boxi Li (Forschungszentrum Jülich)
Session 2
2.3 Boosting Fidelity of Quantum State Preparation via Noise-Aware Variational Training Speaker: Hanrui Wang (MIT)

## Slide 3: Towards Parameterized Quantum Pulses Advantage
Zhiding Liang
University of Notre Dame
Notes: The current pace of hardware development in quantum computing is very fast
We have different technologies
The number of qubits

## Slide 4: Agenda
Compilation Workflow.
  Control System, Software.
  Translation from gate to pulse.
  Single qubit control and two qubit control.
Pulse-level advantage
  Expressivity analysis.
  Time dependent noise model.
Pulse Simulator
  Unitary time evolution.
  Lindblad master equation.
Weyl Chamber
Pulse Ansatz

## Slide 5: Control System
Application Software
Control Software
qc.measure
qubit(0)
qc.measure
qubit(1)

## Slide 6: Control System
Application Software
Control Software
Control Hardware
1
0

## Slide 7: Control System
Stancil, Daniel D., and Gregory T. Byrd. Principles of superconducting quantum computers.
John Wiley & Sons, 2022.
Notes: Junction Parametric Amplifier (JPA) quantum processor (QP) high electron mobility transistor(HEMT)—a type of transistor that is known for producing very low noise.

## Slide 8: Control Hardware
The microwave is used to control the quantum bits.
Krantz, Philip, et al. "A quantum engineer's guide to superconducting qubits." Applied physics reviews 6.2 (2019).
Notes: . (a) Schematic of a typical qubit drive setup. A microwave source supplies a high-frequency signal (ωLO), while an arbitrary waveform generator (AWG) supplies a pulseenvelope (s(t)), sometimes with a low frequency component, ωAWG, generated by the AWG. The IQ-mixer combines the two signals to generate a shaped waveform Vd(t) with a frequency ωd = ωLO ± ωAWG, typically resonant with the qubit.
(b) Example of how a gate sequence is translated into a waveform generated by the AWG. Colors indicate I and Q components.
(c) The action of a Xπ/2 pulse on a |0i state to produce the |−ii = √1 2 (|0i − i|1i) state.

## Slide 9: Control Software
Circuit
Pulse
Result
Scheduling/
Compilation
Execution

## Slide 10: Control Software
Gate- and Pulse-level are two different abstraction layers.

## Slide 11: Gate – Pulse Translation
Single qubit gate to pulse, e.g., X gate.
Two qubit gate to pulse, e.g., CX gate.
Map from gate to pulses

## Slide 12: Gate – Pulse Translation
For single qubit gate: e.g., X gate
Given the Hamiltonian is constant
Map from gate to pulses:

## Slide 13: Gate – Pulse Translation
For single qubit gate: e.g., X gate
Given the Hamiltonian is constant
For two qubit gate: e.g., CZ gate
Given the Hamiltonian is constant
Map from gate to pulses:

## Slide 14: Gate – Pulse Translation
𝑉0 is the amplitude.
φ is the angle.
I = cos(φ) (the ‘in-phase’ component)
Q = sin(φ) (the ‘out-of-phase’ component)
Map from gate to pulses:
Notes: where Ω = (Cd/CΣ)Qzpf and ωq = (E1 − E0) e CΣ = C + Cd is the total capacitance to ground and Q˜ = CΣΦ˙ − CdVd(t) is a renormalized charge variable for the circuit.

## Slide 15: Single Qubit Control
Microwave pulse rotates the qubit around the Bloch sphere.

## Slide 16: Two Qubit Control
For IBM superconducting quantum machines, the minimum 2 qubit control basis is cross resonance. The Hamiltonian of cross resonance can be express as following form:
Since IBM take CX as the 2 qubit basis gate, CX gate only require ZX term, thus, all other terms can be taken as unwanted terms and should be removed by calibration.

## Slide 17: Two Qubit Control
Combining the pulse-level property, previous researchers proposed a method to accelerating the gate speed for RZX(θ), which is called pulse-efficient transpilation [1].
RZX gate also only require ZX term, for achieving RZX(θ), we need to make ZX term tunable. In [1], they make the change of θ proportional to the change of duration and amplitude of the pulse – stretching pulses to use only one echoed cross resonance to represent the RZX(θ).
[1] Earnest, Nathan, Caroline Tornow, and Daniel J. Egger. "Pulse-efficient circuit transpilation for quantum applications on cross-resonance-based hardware." Physical Review Research 3.4 (2021): 043088.
=
~ 1 x
Instead of previous ~ 2 X

## Slide 18: Agenda
Compilation Workflow.
  Control System, Software.
  Translation from gate to pulse.
  Single qubit control and two qubit control.
Pulse-level advantage
  Expressivity analysis.
  Time dependent noise model.
Pulse Simulator
  Unitary time evolution.
  Lindblad master equation.
Weyl Chamber
Pulse Ansatz

## Slide 19: Noise Analysis
Noise on gate level:
Are usually independent among qubits.
Applied after each perfect gate operation.
Noise on pulse level:
Operation and noise are together built in the same model not separate.
Noise are correlated both in time and space.
Noise on real machine.
Approximate picture
Realistic picture

## Slide 20: Expressivity Analysis
Sampling expressivity of single qubit pulse and compare with different single qubit gate operations.
Liang, Zhiding, et al. "Towards Advantages of Parameterized Quantum Pulses." arXiv preprint arXiv:2304.09253 (2023).

## Slide 21: Expressivity Analysis
Give some pulse ansatz design space settings.

## Slide 22: Expressivity Analysis
Expressivity getting better as the increase of qubits number and increase of circuit block layers.

## Slide 23: Entanglement Analysis
Change parameters on 2-qubit cross resonance pulse shift the entanglement power.
Two CR pulses fixed amplitude
Two CR pulses

## Slide 24: Entanglement Analysis
Entanglement capability keep increased with increasing of qubits number and circuit block layers.

## Slide 25: Agenda
Compilation Workflow.
  Control System, Software.
  Translation from gate to pulse.
  Single qubit control and two qubit control.
Pulse-level advantage
  Expressivity analysis.
  Time dependent noise model.
Pulse Simulator
  Unitary time evolution.
  Lindblad master equation.
Weyl Chamber
Pulse Ansatz

## Slide 26: Closed Quantum System Simulation
For a closed quantum system, the dynamics is determined by the Hamiltonian and the initial state.
If we want to controlling this quantum system, the full system Hamiltonian can be expressed as non-controllable drift Hd and controllable terms combined as Hc

## Slide 27: Closed Quantum System Simulation
The non-controllable drift term Hd captures the inherent evolution of the system and interactions that cannot be directly manipulated.
Controllable term (Hc) represent the parts of the Hamiltonian that can be actively manipulated or controlled. They typically involve external fields or control parameters that can be adjusted by an experimenter.

## Slide 28: Closed Quantum System Simulation
describe the strength of signals, which is determined by the user defined pulses.
The system Hamiltonian of closed quantum system illustrated as bellow:

## Slide 29: Closed Quantum System Simulation
describe the strength of signals, which is determined by the user defined pulses.
describes the effects of available physical controls on the system, which is the control Hamiltonian.
The system Hamiltonian of closed quantum system illustrated as bellow:

## Slide 30: Unitary Time Evolution
Schrödinger Equation
SESolver

## Slide 31: Unitary Time Evolution
Schrödinger Equation
Given an initial state and Hamiltonian
SESolver

## Slide 32: Unitary Time Evolution
Schrödinger Equation
SESolver
Given an initial state and Hamiltonian
What state will be in the future

## Slide 33: Unitary Time Evolution
Schrödinger Equation
Given an initial state and Hamiltonian
What state will be in the future
Statically describe the dynamics only for the perfect closed system
SESolver

## Slide 34: Open Quantum System Simulation
Looks familiar :-D
Closed System Hamiltonian Description
Now let’s look at how to describe the open quantum system Hamiltonian.

## Slide 35: Open Quantum System Simulation
Looks familiar :-D
Closed System Hamiltonian Description
Now Different :-P
Open System Hamiltonian Description
Now let’s look at how to describe the open quantum system Hamiltonian.

## Slide 36: Lindblad Master Equation
dynamics of the density matrix
Still familiar
Unitary Evolution
Dissipative Terms
Lis dissipative operators
Lindblad master equation is the key to describe the dynamics of the density matrix in the open quantum system.
is the superoperator
,
Notes: \(L_k\rho L_k^{\dagger}\) corresponds to the term responsible for the decay or relaxation of the system due to the interaction with the environment. It captures the process of the system losing energy to its surroundings.
\(-\frac{1}{2}\{L_k^{\dagger}L_k, \rho\}\) accounts for the dephasing or decoherence effects on the system. It describes how the system's coherence or quantum information can be degraded by interactions with the environment.
The Lindblad master equation combines the coherent evolution governed by the Hamiltonian with the dissipative effects due to the Lindblad operators, providing a comprehensive description of open quantum systems.

## Slide 37: Agenda
Compilation Workflow.
  Control System, Software.
  Translation from gate to pulse.
  Single qubit control and two qubit control.
Pulse-level advantage
  Expressivity analysis.
  Time dependent noise model.
Pulse Simulator
  Unitary time evolution.
  Lindblad master equation.
Weyl Chamber
Pulse Ansatz

## Slide 38: Weyl Chamber
The Weyl Chamber is a geometric representation of all possible two-qubit gates and understanding it can help researchers and practitioners in quantum computing to identify the best gate sequences for achieving a desired transformation.
Represent the time evolution of Hamiltonian in Weyl Chamber:
Notes: \(L_k\rho L_k^{\dagger}\) corresponds to the term responsible for the decay or relaxation of the system due to the interaction with the environment. It captures the process of the system losing energy to its surroundings.
\(-\frac{1}{2}\{L_k^{\dagger}L_k, \rho\}\) accounts for the dephasing or decoherence effects on the system. It describes how the system's coherence or quantum information can be degraded by interactions with the environment.
The Lindblad master equation combines the coherent evolution governed by the Hamiltonian with the dissipative effects due to the Lindblad operators, providing a comprehensive description of open quantum systems.

## Slide 39: Trajectory
Each trajectory on Weyl Chamber indicate one target gate and a set of basis gates.
Notes: \(L_k\rho L_k^{\dagger}\) corresponds to the term responsible for the decay or relaxation of the system due to the interaction with the environment. It captures the process of the system losing energy to its surroundings.
\(-\frac{1}{2}\{L_k^{\dagger}L_k, \rho\}\) accounts for the dephasing or decoherence effects on the system. It describes how the system's coherence or quantum information can be degraded by interactions with the environment.
The Lindblad master equation combines the coherent evolution governed by the Hamiltonian with the dissipative effects due to the Lindblad operators, providing a comprehensive description of open quantum systems.

## Slide 40: Agenda
Compilation Workflow.
  Control System, Software.
  Translation from gate to pulse.
  Single qubit control and two qubit control.
Pulse-level advantage
  Expressivity analysis.
  Time dependent noise model.
Pulse Simulator
  Unitary time evolution.
  Lindblad master equation.
Weyl Chamber
Pulse Ansatz

## Slide 41: Motivation and Challenges
Challenges:
QOC is limited to few qubits since it is computationally expensive.
Most works demonstrate QOC on quantum simulators, however, it is hard to be evaluated on NISQ machines.
Given a unitary matrix, we can use optimal control to find a theoretically best control pulse achieving reduction of pulse latency and increase quantum volumes.

## Slide 42: Attempt on Quantum Neural Network
Can we find an intermediate-level approach between the gate level operations and quantum optimal control?
Can we achieve benefits by doing so?
Liang, Zhiding, et al. "Variational quantum pulse learning." 2022 IEEE International Conference on Quantum Computing and Engineering (QCE). IEEE, 2022.

## Slide 43: Optimization Framework

## Slide 44: Pulse based Compare to Gate based
Pulse based method has higher accuracy than gate based with same depth/latency.
Model | # of Gates | Accuracy
Gate Based | 9 | 0.62
Pulse Based | 9 | 0.71
Gate Based | 12 | 0.68

## Slide 45: Pulse Ansatz on VQAs
Futher Questions:
If we can find a hardware efficient ansatz at the pulse level?
What is a good pulse ansatz?
Liang, Zhiding, et al. "Pan: Pulse ansatz on nisq machines." arXiv preprint arXiv:2208.01215 (2022).

## Slide 46: Framework and Evaluation
Progressive learning fix the problem that non gradient optimizer cannot hold high dimensional parameters, and progressive approaching to target point is also fit the quantum speed limit (QSL) theory.

## Slide 47: Framework and Evaluation
HeH+: average accuracy 99.336%, with 99.895% being the highest achievable accuracy. The absolute difference in energy is 0.003H, close to the requirement of computational chemistry error (0.0016H) with only a toy model.

## Slide 48
Thanks for Listening!
Q & A